## Slide 1: Weather Products and Briefings

## Slide 2: Types of Weather Info
Real time (or nearly so) observations – text products
  METARs
  ASOS/AWOS
  ATIS
  PIREPs
Current Condition Charts
  Surface Analysis Charts
  Weather Depiction Charts
Forecasts
  TAFs
  Graphical Area Forecasts
  Outlook (Prog) Charts
  Winds Aloft
Hazards to Aviation: SIGMets and AIRMets

## Slide 3: METAR METerological Aerodrome Report
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 4: Airport ID and time of observation Time = day of month + hh:mm Zulu SPECI = observation outside usual schedule
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 5
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100
AUTO If the observation was recorded from an automated weather station, AUTO will appear here

## Slide 6: Winds nnn° true direction wind is blowing from (d)ddKT: wind speed in knots ddGddKT means base wind + gusts (>10kt between lull and peak) over last 10 minutes VRB < 6KT or direction changes +/- 60°
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 7: Visibility/Runway Visual Range Greatest horizontal distance at which selected objects can be seen and identified in statute miles (SM) 10 means “10 or greater”; M means “less than”
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 8: Present Weather (Precipitation, Obscuration, etc) 2 letter codes with modifiers; can be combined
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 9: Present Weather (Precipitation, Obscuration, etc)

## Slide 10: Present Weather (Precipitation, Obscuration, etc)

## Slide 12: Sky condition/ceilings condition 1 of 6 codes; ceilings in 00s feet AGL
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 14
FEW012 SCT030 BKN050

## Slide 15: Vertical Visibility
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV005 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044

## Slide 16: Temperature/Dewpoint rounded to nearest whole degree Celsius
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 17: Altimeter current pressure at altitude; no decimal point
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 18: Remarks
KESN 242345Z 32005KT 10SM CLR 07/M06 A3047
KBWI 242354Z 32007KT 10SM FEW150 SCT200 SCT250 07/M08 A3044 RMK AO2 SLP308 T00721083 10122 20072 53026
KLTS 261955Z AUTO 13024G30KT 7SM OVC004 11/11 A2963 RMK AO2 PK WND 12032/53 PRESFR SLP034 T01130111
KHMN 262014Z AUTO 24035G50KT 3/4SM R16/2200V4500FT HZ VV013 15/M02 A2979 RMK AO2 CIG 002 RWY34 SLP044
SPECI KHIE 262008Z AUTO 00000KT 1 1/4SM -SN BR OVC021 M08/M10 A2964 RMK AO2 P0000 T10781100

## Slide 19: Remarks

## Slide 21: PIREPs (Pilot Reports)

## Slide 24
Current Conditions: Surface Analysis Chart

## Slide 25
Surface Analysis Chart

## Slide 26
Weather Depiction Chart

## Slide 28
Weather Depiction Chart

## Slide 29: Terminal Aerodrome Forecast

## Slide 30: Expected meteorological conditions at an airport during a specified period Issued by the National Weather Service TAFs are valid for 24 to 30 hours Wind, visibility, cloud cover, and expected precipitation within a 5-statute-mile radius of the airport center Issued at designated weather service forecast offices (WFOs) Available in both text and graphical formats via aviationweather.gov

## Slide 38: Old-Style Area Forecast (FA)

## Slide 39: Graphical Area Forecast

## Slide 45
Low Level Prog Chart – 12H

## Slide 46
Low Level Prog Chart – 24H

## Slide 47
AIRMETs (Airmen's Meteorological Information)
Description of weather phenomena that may affect aircraft safety.
Compared to SIGMETs, AIRMETs cover less severe weather
  moderate turbulence and icing
  sustained surface winds of 30 knots or more
  restricted visibility over an area at least 3000 square miles.

## Slide 48
AIRMETs (Airmen's Meteorological Information)
AIRMET SIERRA (mountain obscuration or IFR)
    ceilings less than 1000 feet and/or
    visibility less than 3 miles
    affecting over 50% of the area at one time
    extensive mountain obscuration
AIRMET TANGO (turbulence)
    moderate turbulence
    sustained surface winds of 30 knots or greater
    non convective low−level wind shear.
AIRMET ZULU (icing)
    Moderate icing and provides freezing level heights

## Slide 50
SIGMETs (Airmen's Meteorological Information):
Weather advisories concerning safety of all aircraft
Convective
    embedded thunderstorms
    line of thunderstorms
    thunderstorms level 4 or higher
    surface winds > 49 knots
    hail >= 3/4 inches
    Tornadoes
  Non-Convective (turbulence, icing, etc)

## Slide 51: SigMets