## Slide 1: Weather Theory

## Slide 2: Topics Covered
General Principles
Circulation and Wind
Air Masses and Fronts
Vertical Motion of the Atmosphere
Clouds and Precipitation
Thunderstorms
Other Causes of Turbulence
Obstructions to Visibility
Icing

## Slide 3: All VFR flying occurs in the slice of atmosphere called the “troposphere.”

## Slide 4: All VFR flying occurs in the slice of atmosphere called the “troposphere.”
75% of total atmospheric mass
99% of total water vapor and aerosols
Virtually all weather

## Slide 5: Atmospheric Gases
Nitrogen : 78%
Oxygen: 21%
Trace gases: 1%
Refers to dry air
Constant both
Horizontally
Vertically

## Slide 6
Water vapor
Is not uniformly distributed either across the surface or vertically
Varies from approximately 1% - 4% of the atmosphere
Creates atmospheric instability

## Slide 7: Radiation from the sun heats the earth’s surface. This heating is uneven and varies on a global scale with the angle of incidence of the sun’s rays.

## Slide 8: Local heating is also uneven and is caused by different reflective properties of soil, vegetation, manmade surfaces, and water.

## Slide 9: Every physical process of weather is accompanied by or is a result of unequal heating of the Earth’s surface

## Slide 10: Warm Air Cool Air
Rises
Falls

## Slide 12: Global scale: air warmed at lower latitudes rises cold air from the poles falls to replace it…

## Slide 13: Local Scale: surfaces of varying reflectivity produce areas of faster-rising air.

## Slide 14
  Atmospheric Pressure
  and
  Temperature
  Decrease
  with
  Altitude

## Slide 15: Imagine a column of air one foot square, rising from sea level to the top of the atmosphere. The weight of the entire column of air presses on anything located at the bottom of the column.

## Slide 16: Compare this with a column of air reaching from 7,500 feet to the top of the atmosphere. There is less mass pressing on objects located at this surface. The air at the bottom of this column is less dense.
surface
surface

## Slide 17: Standard pressure decreases about 1 inch of mercury for every 1000 foot gain in altitude.

## Slide 18: In the troposphere, temperature also decreases as altitude increases. The average lapse rate of temperature with altitude is 3.5° F or 2 ° C per 1000 feet. (It is greater for dry air, less for moist air.)

## Slide 19
  Warm air
  can hold more
  water vapor
  than
  cold air

## Slide 20: Water enters and leaves the atmosphere through a variety of processes.

## Slide 21: Atmosphere contains moisture in the form of water vapor. Amount of moisture present in the atmosphere is dependent upon the temperature of the air. Every 20 °F increase in temperature doubles the amount of moisture the air can hold. Conversely, a decrease of 20 °F cuts the capacity in half.” Temperature largely determines the maximum amount of water vapor air can hold

## Slide 22
  Areas of
  high pressure
  will move to occupy
  areas of
  low pressure

## Slide 23: Wind
Wind is the air in motion relative to the surface of the Earth
Winds cause the formation, dissipation, and redistribution of weather.
Winds affect aircraft during all phases of flight

## Slide 24: Three primary forces affect the flow of wind on a large scale:
Pressure gradient force
Coriolis force
Friction

## Slide 25: Wind is driven by pressure differences which create a force called the Pressure Gradient Force. This force causes the wind to blow in an attempt to equalize pressure differences.

## Slide 26: Areas of equal pressure are depicted with lines called “isobars” on this surface analysis chart.
Notes: The wind would flow from high to low pressure if the PGF was the only force acting on it. However, because of the Earth’s rotation, there is a second force called the Coriolis force that affects the direction of wind flow.

## Slide 27: Overlaid on satellite

## Slide 28: Coriolis Force
A moving mass travels in a straight line until acted on by some outside force.
If one views the moving mass from a rotating platform, the path of the moving mass relative to his platform appears to be deflected or curved.

## Slide 30: The Coriolis force is greatest at the poles and least at the equator. It is proportional to the speed of the wind
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 31: In the upper air, friction is not a factor. The wind starts moving initially from high to low pressure, but as soon as it starts moving, Coriolis force turns it to the right.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 32: When PGF and Coriolis force are in balance, the wind now moves parallel to the contours. Air flows clockwise around areas of high pressure and counter-clockwise around areas of low pressure.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 33: Windy.com

## Slide 34: Friction
Within in the friction layer (from the surface to 2,000-3,000 feet AGL) friction between the molecules of air and the terrain surface slows the wind.
The direction of the friction force is 180 degrees from the direction of the wind.

## Slide 35: When friction is added to the PGF and Coriolis force, it slows the wind. Since Coriolis force is directly proportional to wind speed, it also slows, and the wind is no longer being pulled quite so strongly to the right.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 36: The result is that at the surface, wind spirals clockwise and outward from high pressure, and counter-clockwise and inward to low pressure. In very rugged terrain the winds may have little relation to pressure gradient because the friction force outweighs the other two forces.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 38
Local winds are mainly driven by pressure gradient force
They are over a smaller area, and have a shorter life span, so Coriolis force does not have as much time to act.
PGF is set in motion by local warming and cooling of surfaces.

## Slide 39: Wind blows from a high-pressure cool surface to a low-pressure warm surface. This is easiest to see when larger-scale wind patterns are weak.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 40: This is an example of a local wind called “sea breeze.” Air over land warms faster than air over water.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 41: At night this process reverses, as land also cools down faster than water when the sun sets. This is called a “land breeze.”
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 42: A similar phenomenon occurs in mountains, where the sloping terrain both heats and cools faster than the valleys, producing “valley breeze” and “mountain breeze.”
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 43: Air Masses and Fronts

## Slide 44: Air Mass
An air mass is a large body of air with generally uniform temperature and humidity.
The longer the air mass stays over its source region, the more likely it will acquire the properties of the surface below.

## Slide 45: North America will typically have more than one type of air mass present at any given time.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 46: Fronts
Air masses can control the weather for relatively long time periods ranging from days to months.
A front is a boundary or transition zone between two air masses.
Most weather occurs along fronts.

## Slide 47: Fronts are depicted on weather charts with these symbols.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 48: Fronts also have a vertical structure. Cold fronts have steep slopes, and the warm air is forced up abruptly. This often leads to a narrow band of showers and thunderstorms at or just ahead of the front.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 49: Warm fronts typically have a more gentle slope, so the warm air rises gradually. This favors the development of widespread cloudiness and precipitation along the front.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 50: Stationary frontal slope can vary, but clouds and precipitation will still form in the warm rising air along the front.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 51: Cold fronts typically move faster than warm fronts, so in time they catch up to them. Where the two fronts merge, an occluded front forms and the rising warm air is lifted even farther.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 52: Vertical Motion of the Atmosphere

## Slide 53: Atmospheric Stability
The stability of the atmosphere depends on its ability to resist vertical motion.
A stable atmosphere makes vertical movement difficult, and small vertical disturbances dampen and disappear.
In an unstable atmosphere, small vertical air movements tend to become larger, resulting in turbulence, convective activity, extensive clouds, and severe weather.

## Slide 54: Adiabatic Process 1.0 -- Hot Air Rises
Rising air expands and cools due to the decrease in air pressure as altitude increases.

## Slide 55: Adiabatic Process 2.0 – Moist Air Rises Faster
Moist air is lighter and cools more slowly than dry air. So It rises faster and must rise higher before its temperature cools to that of the surrounding air. This makes moist air inherently unstable.

## Slide 56: Sources of Vertical Motion of Air
Orographic
Frictional
Frontal Lift
Buoyancy

## Slide 57: Winds blowing across mountains and valleys cause the moving air to alternately ascend and descend. The resulting expansional cooling and compressional warming of air creates clouds and precipitation.
Orographic Lifting
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 58: Wind spirals clockwise/outward from high pressure; counterclockwise/ inward towards low pressure. Over surface highs, the air sinks, compresses, and warms, causing clouds to dissipate. Over surface lows the air rises, expands, and cools, favoring the formation of clouds and precipitation.
Frictional Effects
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 59: Frontal lift occurs when the denser air of a cold front wedges under the warm, less dense air of the warm front it is overrunning. Clouds and precipitation form.
Frontal Lift
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 60: Air near the ground warms at different rates depending on the insular and reflective properties of the ground with which it is in contact. The warm air rises faster than the cool air, creating “bubbles of turbulence.
Buoyancy
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 61
Temperature inversions
Areas where the normal decrease in air temperature with increasing altitude is reversed and air above the ground is warmer than the air below it.
A warm, less dense air mass moves over a dense, cold air mass (Great Lakes in early summer)
Radiational inversion: surface cooling by longwave radiation emission into space. Pronounced on clear, dry nights. The air closer to the surface cools faster than the air above. Usually dissipates when the surface is warmed by the sun rising.

## Slide 62
Temperature inversions
Inversions block the normal circulatory flow of the atmosphere; the air underneath an inversion layer is trapped. Hazy conditions often prevail.

## Slide 63: Clouds and Precipitation

## Slide 64
To review:
Warm air holds more moisture than cold air
Warm air rises
Air cools as it rises
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 65
The moisture content of the air is described by two related concepts:
Relative humidity
Dewpoint
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 66: Humidity is the amount of water vapor present in the atmosphere at a given time. Relative humidity is the actual amount of moisture in the air compared to the total amount of moisture the air could hold at that temperature.
Relative humidity

## Slide 67: Dewpoint is the temperature below which an air parcel cannot hold any more water. When temperature = dewpoint, water condenses out of the air in the form of dew, fog, frost, clouds, rain, or snow.
Dewpoint

## Slide 68
Air cools as it rises
When the air rises, and its temperature falls, to the point where
temperature = dewpoint
a cloud forms.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 69
Clouds
A cloud is a visible aggregate of minute water droplets and/or ice particles in the atmosphere above the Earth’s surface.
Fog differs from cloud only in that the base of fog is at the Earth’s surface while clouds are above the surface.
Clouds form in the atmosphere as a result of condensation of water vapor in rising currents of air, or by the evaporation of the lowest layer of fog.
Rising currents of air are necessary for the formation of vertically deep clouds capable of producing precipitation heavier than light intensity.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 70
Clouds – cloud types defined by height and shape
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 71
Stratus (strata = flat layers)
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 72
Cumulus = “heap or pile”
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 73
Nimbus = “rain”
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 74
Clouds – cloud types
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 75
Precipitation
Precipitation is any of the forms of water particles, whether liquid or solid, that fall from the atmosphere and reach the ground.
drizzle
rain
snow
snow grains
ice crystals
ice pellets
hail
small hail/snow pellets
Precipitation formation requires three ingredients:
water vapor
sufficient lift to condense the water vapor into clouds
a growth process that allows cloud droplets to grow large and heavy enough to fall as precipitation.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 76
Formation of Precipitation
Cloud droplets and/or ice crystals are too small and light to fall to the ground as precipitation.
Collisions occur between cloud droplets of varying size and different fall speeds, sticking together or coalescing to form larger drops.
The drops become too large to be suspended in the air, and they fall to the ground as rain.

## Slide 77: Thunderstorms and Turbulence

## Slide 78
Thunderstorms
Extensive vertical development
Unstable and turbulent
Contain large amounts of moisture
Produce a number of hazards to aviation

## Slide 79
Requirements for thunderstorm formation:
Water vapor
Unstable air
Lift
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 80
Thunderstorms have a predictable life cycle
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 81
Towering cumulus
The distinguishing feature of the towering cumulus stage is a strong convective updraft. The updraft is a bubble of warm, rising air concentrated near the top of the cloud which leaves a cloudy trail in its wake. Updraft speeds can exceed 3,000 feet per minute.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 82
Mature
The cell transitions to the mature stage when precipitation reaches the surface.
Precipitation descends through the cloud and drags the adjacent air downward, creating a strong downdraft alongside the updraft.
Weather hazards reach peak intensity toward the end of the mature stage.
Notes: It causes wind to deflect to the right in the Northern Hemisphere.

## Slide 84
Dissipating
The dissipating stage is marked by a strong downdraft embedded within the area of precipitation. Subsiding air replaces the updraft throughout the cloud, effectively cutting off the supply of moisture provided by the updraft. Precipitation tapers off and ends. Compression warms the subsiding air and the relative humidity drops.

## Slide 85: Thunderstorm Hazards
Lightning
Icing
Hail
Rapid Altimeter Changes
Static Electricity
Tornados
Turbulence
Adverse Wind
Downbursts

## Slide 86
Turbulence
Gust loads can be severe enough to stall an aircraft at maneuvering speed or to cause structural damage at cruising speed. The strongest turbulence occurs with shear between updrafts and downdrafts. Outside the cumulonimbus cloud, turbulence has been encountered several thousand feet above, and 20 miles laterally from, a severe storm.
Turbulence is present in all thunderstorms. Severe or extreme turbulence is common.

## Slide 87
Turbulence
The wind-shear zone between the gust front and surrounding air is very turbulent airspace. The surface position of the gust front can be identified by a line of dust or debris along the ground, a line of spray along bodies of water, or a shelf cloud as seen here.

## Slide 88
Adverse winds
Adverse winds are always found within thunderstorms and often many miles away from the precipitation area. The area along and immediately behind the gust front is particularly dangerous because this is where rapid and sometimes drastic changes in surface winds occur.

## Slide 89
Adverse winds
Crosswinds, gusts, sudden wind shifts, and downbursts can lead to a crash during takeoffs, approaches, and landings.

## Slide 90
Low level wind shear
While microbursts are often associated with thunderstorms, they can occur far away from visible precipitation.

## Slide 91: Other Causes of Turbulence
Convection
Mechanical Turbulence
  Mountain Waves
  Wind Shear
  Temperature Inversion
  Clear Air Turbulence

## Slide 92: Obstructions to Visibility
Fog
Mist
Haze
Smoke
Precipitation
Blowing Snow
Dust Storms
Sandstorms
Volcanic Ash

## Slide 93
Fog
Fog forms when the temperature of the air and the dewpoint are the same. This may occur through cooling of air or by adding moisture. Fog seldom forms when there is a more than 2°C (4°F) difference between the air temperature and the dewpoint.
Fogs caused by cooling of air | Fogs caused by adding moisture
Radiation fog | Frontal fog
Advection fog | Steam fog
Upslope fog | 

## Slide 94
Fogs caused by cooling of air
Radiation fog is produced over a land area when radiational cooling reduces the air temperature to or below its dewpoint. | 
Advection fog forms when moist air moves over a colder surface and cools below its dewpoint. | 
Upslope fog forms as a result of moist, stable air being adiabatically cooled to or below its dewpoint as it moves up sloping terrain. | 

## Slide 95
Fogs caused by adding moisture
Frontal fog is formed when warm, moist air is lifted over a front. If the cold air below is near its dewpoint, evaporation from the precipitation may saturate the cold air and form fog. It is most commonly associated with warm fronts, but can occur with other fronts as well. | 
Steam fog is formed when very cold air moves across relatively warm water. It is commonly observed over lakes and streams on cold autumn mornings, and over the ocean during the winter when cold air masses move off the continents and ice shelves. | 

## Slide 96: Icing: Two Types (only one is weather)
Structural Icing
Engine icing
  Carburetor icing (aspirated engines)
  High ice/water content (turbine engines)
Notes: Icing can occur whenever the air is below 32F/0C and there is moisture present. In turbulent air like thunderstorms, the danger of rapid clear icing is especially high. This occurs because in the updrafts, water can become supercooled (between 0 and -15C) but will not freeze until presented with a surface – like the skin of an airplane.

## Slide 97: Icing Factors
Structural airframe icing occurs when supercooled water comes into contact with aircraft surfaces
Clear ice can occur at any altitude above the freezing level
High altitude precipitation may be clear, rime, or mixed
Icing can occur anytime the temperature approaches 0 °C and visible moisture is present.
The heaviest icing hazards occur in clouds below 6,500 ft
Altostratus clouds (~6,500 – 20,000 ft) also contain moderate icing hazards
Clouds are infrequent above 20,000 ft, making high altitudes less of an icing hazard